Time: Before 7/26/18

Initial tests of the mito systems involved either pure POPC or 80%POPC and 20%DOPE. The rationale for the lipids were than POPC is quite flat, a good background lipid to for comparing with negative lipids. DOPE was chosen because it’s tails are the same composition as CL (once it’s updated).
Generating flat systems: Flat equilibrium simulations with each composition were run, then new bilayers were created using the average apl, to feed into bumpy. The flat systems were run with 100 lipids per leaflet, 100mM NACL for neutral (what for CL?)

flat systems are in /homekevin/hdd/Projects/mito/reference_files/flat_bilayers, with the flat sims in charmm-gui/gromacs. The new flat sims were generated by using the scale_flat_bilayers function in git repos /python/misc, with the scale factor being the average x dim of the last 20 ns of 50ns flat eq over the final frame

Choosing zo estimates: zos were taken from calculated values from bumpy paper. They’re from 330K and our simulations are at 310K, but DMPC shows basically no difference (0.01) between 330 and 300K so we’re alright. The 20% DOPE zo was estimated as 0.8 * (zo_POPC) + 0.2 (zo_DOPE). The zo of POPC is 0.96 nm, DOPE = 0.83 nm
Geometric choices: Chose a cylinder radius of 10 for diameter = 20 nm. The length of the cylinder was chosen to be 30 nm, to be able to fit 3 ATP synthase dimers (new Davies paper estimates a ~13 nm interdimer distance). The flat area was chosen to be equal to the surface area of the bilayer cylinder.
A_cylinder = 30 * 2 * pi * 10 = 1885 nm^2
A_flat = (L_flat ^2) – pi(20^2) # 20 = r_junction + r_cylinder
L_flat = sqrt(A_flat + pi * 20^2) = 56 nm
Did not change buffer between images
Dummy particles: Each system was simulated with and without bracketing dummy particles, with 5 nm thickness and default lateral spacing
Simulation parameters:
T=310K

Results: See /home/kevin/hdd/Projects/mito/analysis/videos/initial_sims
The dummy particles keep everything in place as expected. The non-dummy systems deform but do not collapse. Unfortunately, the fluctuations for the pure POPC system (and maybe the PE system) lead to periodic images interacting in the z direction.
An anecdotal thing is that the PE system deformed less, and seemed to retain more of a cylinder!

8/3/18
The zo of the new 4-chain CL is 0.903 +/- 0.004 nm (se), for no salt. Rerunning with salt because the system reached across periodic boundaries